## Slide 1: River Reintroduction into Maurepas Swamp & West Short Lake Pontchartrain Risk Reduction Project Combined Project Overview & Challenges
presented by: Leah B. Read, PE AECOM

## Slide 2
Maurepas / WSLP
Big Picture
Maurepas runs 5 ½ miles N - S
WSLP-111, -112 & -113
Share Common N-S Corridor
Separate 2500-ft N of US-61
Maurepas Continues North, WSLP Heads East
Gramercy
Garyville
Conveyance Channel
WSLP / Maurepas Shared Features
WSLP Separate Alignment
New Orleans 25 miles
Maurepas Purpose is to combat Saltwater Intrusion
CPRA

## Slide 3: Maurepas Project History
CPRA
- First major design phase in early 2000’s
- LDNR’s significant design effort started post-Katrina
- First discussed / planned in 1990’s
Utility Corridor
Camp
- Shifted to CPRA (OCPR) and restarted ~2010, paused ~2013
- Formally tied (as mitigation) to WSLP Project this year

## Slide 4: Maurepas Project Overview
CPRA
- Intended to Benefit ~45,000 acres
- Miss River Intake Structure
- Affects St. John the Baptist
& St. James Parishes
- 2 Roadway Crossings (River Rd. & Airline Hwy.)
- 2 Railroad Crossings
- 2,000-cfs Freshwater Diversion from MR to Maur. Swamp
- 1 Interstate Crossing
Utility Corridor
Camp

## Slide 5: Maurepas Project Overview
CPRA
- Primary aim is to reintroduce freshwater and nutrients into swamp. Some sediment will also be introduced.
- Extensive calibration & examination of ADCIRC modeling to determine dispersal.
- Total Nitrogen, Total Phosphorous, & Salinity are the primary nutrients/properties examined.

## Slide 6
CPRA
- Weirs to be installed at Bourgeois Canal & Bayou Secret at Blind River discharge points. Purpose is to avoid short-circuiting of diversion’s output into river (would reduce retention time in target improvement zone).
- Embankment cuts in existing logging RR spur to promote water circulation.
Maurepas Project Overview

## Slide 7
Project Challenges – Mississippi River
CPRA
Intake Headworks
Sedimentation Basin
- Headworks housing 3 – 10ft x 10ft sluice gates to be constructed within MR Levee via cofferdam system
- River Rd. construction for channel & WSLP features to be phased
River Rd. Crossings

## Slide 8
AECOM
Project Challenges – Industrial Development
CPRA
2013 Miss River Headworks Location
Current Miss River Headworks Location

## Slide 9
Project Challenges – Industrial Development
CPRA
CN RR to Airline Hwy, Current
CN RR to Airline Hwy, 2013
CN RR crossing expanded to 4 rail lines
previously 2
KCS RR merged with CP.
Crossing expanded from 1 to 2 lines, including future Amtrak

## Slide 10
Project Challenges – WSLP Integration
CPRA
- All features must fit within same 300-ft ROW.
- Many drainage patterns developed for Maurepas Project must be re-routed, and additional infrastructure added, because of WSLP Flood Risk Reduction features.
- Stability of many features must be re-examined because of addition of adjacent levee / floodwall.

## Slide 11: River Reintroduction into Maurepas Swamp & WSLP Risk Reduction Project Combined Project Overview & Challenges Thank You! Contact Information: Leah B. Read, PE leah.read@aecom.com (504) 586 – 8111 (office)
CPRA